## Slide 1
Charles Hartsell & John Mitchell
Bama Racing Innovation

## Slide 2: Data Acquisition System
Arduino MEGA 2560
Data Gathered:
  Drive Axle RPM
  Engine RPM
  Vehicle Acceleration
  CVT Temperature

## Slide 3: Data Logging
Serial Interface with in-vehicle micro SD card
Logs data from sensors:
  Engine RPM
  Axle RPM
  Acceleration
CVT ratio determined using Engine & Axle RPM

## Slide 4: Driver Interface
16x2 LCD Display:
  Current Speed
  Hour meter
  Odometer
  Tachometer

## Slide 5: Engine RPM Sensor
Capacitive pickup on spark plug wire
Noisy input
74221 monostable multivibrator (aka “one-shot”) used to provide clean rectangular pulse to Arduino

## Slide 6: Axle RPM Sensor
GM camshaft position sensor (inductive pickup)
Op-Amp circuit to boost the signal to 5V logic level

## Slide 7: 3-Axis Accelerometer
I2C interface with microcontroller through 3.3 to 5V Logic Leveler
Selectable range of ±2g/ ±4g/ ±8g
Secondary Speed measurement
Vehicle Orientation

## Slide 8: Power Consumption
Typical Current Draw:
  Brake/Reverse Light: 100 mA each
  Reverse Alarm: 70 mA
  Arduino: 25 mA under load
  Sensors/Screen: 20 mA typical
Significant power consumption by Data Acquisition System
5 Ah battery chosen for long battery life (approximately 55 hours)

## Slide 9: Dashboard
Low-Profile for Driver Visibility
3D Printed for ease of manufacture and light weight
Total Weight (inc. DAS): ~4 lbs

## Slide 11: Cost Report
Arduino MEGA: 45.95
Display: 8.20
Accelerometer: 9.95
Position Sensor: 25.28
Temp Sensor: 1.50
Misc: ~20.00
Total: 110.88
Entire Electrical Cost: 391.78